In the framework of ADIRA project (www.adira.info) funded by the European Comission, the Jordan University of Science & Technology (JUST) is interested in installing a desalination unit using the Reverse Osmosis (RO) technology. The RO unit should be operated utilizing the solar energy by using Photo Voltaic panels (PV-panels). The complete unit (PV-RO) will be placed on the building of an NGO in Hartha village (about 15 km north of Irbid city). The origin of the main parts of the PV-RO unit should be from the EU or MENA countries.

Interested companies to install the complete unit (RO+PV) are urged to submit their offers to the University. Technical Details are as follows:

- Feed water : Brackish water with 4000 ppm maximum

- Production Capacity: half cubic meter per day

- Complete pretreatment and post treatment units

- Feed, Permeate and brine tanks

- The required PV panels with the required batteries and  electricity inverters

- Complete installation of the unit at Hartha village

- One year warranty for the main components (PV, membranes, pumps, etc.)

- Maintenance and spare parts for one year is of benefit

| Tender No. | Description | Price of Documents | Dead Line |
| --- | --- | --- | --- |
| 85/2006 | In the framework of ADIRA project (www.adira.info) funded by the European Commission, the Jordan University of Science & Technology (JUST) is interested in installing a desalination unit using the Reverse Osmosis (RO) technology | 15 JD | 28/11/2006 |

Interested participants should contact the Tenders Department / JUST to receive the Tenders' Documents after delivering the followings:

- Valid Apprentices License

- Valid Registration Certificate

General Condition:

- A Bank Guarantee equivalent to 5% of the Tenders' Amount should be submitted with the offer.

- Three copies of the offer should be submitted (one original) each in separate, closed and sealed envelop marked with the Tenders' No. and the participant's name and address.

- The offers should be delivered through "the Tenders' Box" no later than 10:30 AM. The Tenders will be opened at 1 PM on  the same day.

- Any offer which is not fully in accordance with these conditions and the general Tenders conditions will be disregarded.

- For more details you may see the following website:

www.just.edu.jo